## Slide 1: Theory & Implementation of Grover’s Algorithm in IBM’s QISkit OpenQASM 2.0 Representation
GEORGE DAVILA, ALI AL KOBAISI, TYRONE THAMES

## Slide 2: OUTLINE
Basics of Software/Hardware
  Backend
  Basic examples of circuits on IBMQX4
Grover’s Algorithm:
  The Problem
  Conceptual basics
Grover’s Algorithm:
  Implementation on IBMQX
  Results

## Slide 3: IBMQX4 CHIP
Parameters of the chip
5 qubit chip
ωR i = Resonant frequency of readout resonator R i
ω i = qubit frequency
δi = anharmonicity, difference b/w freq of state 1→ 2 transmission and freq of state 0→1 transition
χ = qubit-cavity coupling strength

## Slide 4: PHYSICS OF QUBIT-CAVITY SYSTEM
Described by cavity quantum electrodynamics (cQED)
Vacuum particles disturb the qubit → don’t have perfect coherence
Constitutes a Hybrid Quantum System → Dissipates into environment
Qubit Cavity

## Slide 5: PHYSICS OF QUBIT-CAVITY SYSTEM
Keep at low temperature T = 0.021 K to help preserve coherence
(Retrived April 7th appx 15:00)

## Slide 6: SIMPLE EXAMPLES OF IMPLEMENTATION
Should yield result of 1 on 00000, but since it’s using actual qubit it decoheres and leaks into the 00001 state a bit
No entanglement here

## Slide 7
Ibmqx4 chip
00001
00000
Simulation of circuit

## Slide 8: GROVER’S ALGORITHM QISKIT OPENQASM 2.0 REPRESENTATION

## Slide 9: THE PROBLEM
Given a Boolean black box 𝑓 : {0, 1, …, 2𝑛−1} → {0, 1} that indicates whether a given item is marked.
The problem is to find the marked item given that one exists.

## Slide 10: GROVER’S ALGORITHM
Starts by preparing the superposition of all bases using Hadamard gates. Repeat sqrt(𝑁) times: Apply, 𝑓, the black box operation. Apply reflection across the average.

## Slide 11: GEOMETRICALLY
The black box (phase oracle) reflects the current state around the uniform superposition of all unmarked bases.

## Slide 12: GROVER’S DIFFUSION OPERATION
After application of the oracle, the state can be pushed towards 𝜔 by a reflection around |s⟩.
The operation for this reflection is:
𝑉 = 𝐼 - 2|s⟩⟨s| = 𝐻 (𝐼 - 2|0⟩⟨0|) 𝐻

## Slide 13: N = 16
The process can be repeated 3 times

## Slide 14: SUPERPOSITION OF ALL BASES

## Slide 15: PHASE ORACLE
f can be written as a reversible operation as:

## Slide 16: FIRST OPERATION / REFLECTION

## Slide 17: REFLECTION ACROSS THE AVERAGE
After 2nd reflection:
𝑉 = 𝐼 - 2|s⟩⟨s|

## Slide 18: IMPLEMENTATION
Prepare the state of superposition of all bases using Hadamard gates.
for i in range(N):
circuit.h(q_register[i])

## Slide 19: IMPLEMENTATION / REFLECTION ABOUT |000…0⟩
We need operator:
I - 2|0⟩⟨0|
that maps:
|0⟩ ⟼ -|0⟩
|x⟩ ⟼ |x⟩
Pauli Z gate:
|0⟩ ⟼ |0⟩
|1⟩ ⟼ -|1⟩
Controlled Z:
|00⟩ ⟼ |00⟩
|01⟩ ⟼ |01⟩
|10⟩ ⟼ |10⟩
|11⟩ ⟼ -|11⟩

## Slide 20: IMPLEMENTATION / REFLECTION USING CONTROLLED Z
NOT Controlled Z NOT:
|00⟩ ⟼ -|00⟩
|01⟩ ⟼ |01⟩
|10⟩ ⟼ |10⟩
|11⟩ ⟼ |11⟩
NOT⊗n Cn-1Z NOT⊗n
Giacomo Nannicini, “An Introduction to Quantum Computing, Without the Physics”, 2018

## Slide 21: IMPLEMENTATION / CONTROLLED Z USING CNOT
There is no Controlled Z operator in QISKit.
But Z operator is equal to:
Z = H NOT H
Therefore Controlled Z can be written as:
CZ = (I⊗H) CNOT (I⊗H)

## Slide 22: IMPLEMENTATION / N CONTROLLED NOT
Adriano Barenco et. al, “Elementary gates for quantum computation", Quantum Physics, 1995, Lemma 7.2.

## Slide 23: IMPLEMENTATION / PHASE ORACLE
|00⟩ ⟼ -|00⟩
|10⟩ ⟼ -|10⟩
|11⟩ ⟼ -|11⟩
|01⟩ ⟼ -|01⟩

## Slide 24: IMPLEMENTATION / REFLECTION ACROSS AVERAGE
So:
𝐼 - 2|s⟩⟨s|
can be implemented as:
H⊗n NOT⊗n CZ NOT⊗n H⊗n
For 2 qbits: